## Slide 1: Workshop on the Mining Sector Presentation to The Office of the Principal Accountant General (Audit), Bihar Part 2 Optimising Mineral Development in Bihar Brookings Institution India Center, New Delhi June 25, 2020
BROOKINGS INDIA
QUALITY. INDEPENDENCE. IMPACT

## Slide 2: Contents
Mineral potential and opportunities in Bihar
Mineral value chain and entrepreneurial ecosystem
Prudent mineral exploration policy for India

## Slide 3: Mineral Potential and Opportunities in Bihar

## Slide 4: Geology of Bihar
About 10% of Bihar consists of hard rocks ranging from Archean to Mesozoic Age
About 30% area consists of hard rocks with shallow Gangetic Basin alluvial cover (max 500 m thickness)
About 60% area consists of thick Gangetic Basin alluvial cover (more than 500 m thickness)
Map by GSI

## Slide 5: Mineral Potential of Bihar
  Copper
  Uranium
  Gold - Silver
  Platinum group (PGE)
  REE – Hard rock
  Lithium
  Nb-Ta
  Nickel chrome
  Iron ore (magnetite)
  Coloured gemstones
  Graphite
  Vanadium - Titanium
  Lead Zinc
  Mica
  Feldspar
  Talc – steatite
  Granite
  Marble
Chota Nagpur Gneissic Complex
  Pyrite
  Limestone
  Phosphate
  Dolomite
Vindhyans
  Coal
Gondwana
  Potash
  Salt
  Bauxite
  REE – Tertiary clay
Tertiary
  Construction sand
  Silica Sand
Quaternary
  Heavy mineral sand
  Construction Aggregates
  China clay
  Fire clay
Tertiary / Quaternary
Geology
Minerals

## Slide 6: Mineral Inventory of Bihar (IBM Data)
Source: Indian Bureau of Mines

## Slide 7: Coal Resource of Bihar (IBM Data)

## Slide 8: Mineral Resource in Bihar (GoB)
Mineral | Minerals Availability in India* | Minerals availability in Bihar*
Limestone | 75678.89 | 210.85
Pyrites | 98.79 | 53.41
Quartz | 2402.18 | 10.83
Silica sand | - | 5.25
Feldspar | 31.28 | 4.84
Quartzite | 305.07 | 3.02
Bauxite | 2462.43 | 1.5
China clay | 1042.46 | 1.2
Magnetite stone | 3407.82 | 0.59
Decorative stone | 1047.42mcub | 67.91mcub
Slate/Phylite | - | 4.07mcub
Gold ore | 1778.79 | 128.88 Gold mineral 0.1-0.6 gm / ton gold ore
Source: Administrative report 2018-19 of the Department of Mines and Geology, GOB
* Figures in million metric tons, unless otherwise indicated

## Slide 9: Mineral Revenue in Bihar
Source: Administrative report 2018-19 of the Department of Mines and Geology, GOB
Revenue Collection from the Mining Sector |  |  | 
figure in Lakh |  |  | 
 | 2017-18 | 2018-19 | 2019-20
Major Mineral |  |  | 
Lime Stone | 152.85 | 588.59 | 1004.11
Minor Mineral |  |  | 
Sand | 41066.77 | 76740.68 | 87431.42
Work division | 41893.12 | 43687.67 | 52396.58
Stone/Crusher | 12784.91 | 16283.65 | 9104.26
Bricks | 3934.47 | 4154.60 | 6218.30
Ordinary earth | 485.42 | 702.41 | 417.16
Transit Pass | 1039.12 | 0.00 | 0.00
Penalty/Others | 1636.48 | 6382.73 | 4355.64
Arrears |  |  | 
Certificate Case | 174.31 | 220.03 | 182.91
Bihar State Mining Corporation | 5100.00 | 6917.00 | NA

## Slide 10: Yearwise Revenue Target and Collection from the Mining Sector - Bihar
Yearwise Revenue target and collection from the Mining Sector |  |  | 
figure in Crore |  |  | 
Year | Target | Collection | percentage
2015-16 | 1000.00 | 971.00 | 97.10
2016-17 | 1100.00 | 994.10 | 90.37
2017-18 | 1350.00 | 1082.67 | 80.20
2018-19 | 1600.00 | 1556.77 | 97.30
2019-20 | 2000.00 | 1611.52 | 80.57
Source: Administrative report 2018-19 of the Department of Mines and Geology, GOB

## Slide 11: Mineral Exploration in Bihar (By GSI)
Year | Number of Projects | Commodities | Location (Districts)
20-21 | 8 | Gold, REE, RM, Li, Potash, Fe | Jamui, Banka, West Champaran, Gaya, Munger, Rohtas
19-20 | 14 | REE, RM, Al, potash, gold, limestone, Fe, Li, Ti, V, Ga, PGE, Cr, Ni, Ti | Jamui, Banka, West Champaran, Gaya, Rohtas, Munger, Nawada, Bhagalpur
18-19 | 7 | Cr, Ni, PGE, REE, RM, limestone, Fe, potash, Ti, V, Ga | Gaya, Banka, Rohtas, Jamui,
17-18 | 6 | REE, RM, Ti, V, Ga, Fe, potash | Jamui, Rohtas, Gaya
16-17 | 6 | Fe, Ti, Au, Cr, Ni, PGE, REE, RM, potash | Gaya, West Champaran, Jamui, Kaimur
15-16 | 6 | Fe, Au, REE, RM, potash | Gaya, West Champaran, Jamui, Kaimur
14–15 | 1 | Au | Gaya
13-14 | 1 | Au | Jamui
12-13 | 2 | Au | Jamui, Gaya
10-11 | 2 | Au | Jamui, Gaya
None of the exploration carried out by GSI has led to establishment of a Geological Resource or discovery of any economic deposit

## Slide 12: Baseline Data Generation: By GSI
GSI’s geological map (1:50k scale) is completed. Specialised thematic mapping is being carried out
GSI is collecting extensive geochemical data through its National Geochemical Mapping (NGCM) Program
GSI’s National Aero-geophysical Survey Program has covered about 5% of Bihar
This is one of the best baseline geological information in terms of quality.
Bihar would require a more extensive coverage of National Aero-geophysical Survey Program data covering the entire region south of Ganga and the foothills of Himalayas

## Slide 13: Mineral Value Chain and Entrepreneurial Ecosystem

## Slide 14: Mineral Value Chain and Entrepreneurial Ecosystem
Obvious Geological Potential
Mineral Deposit Discovery
Mining
And
Beneficiation
Metal Extraction
Product Development
Recycle and Reuse
Mineral Targeting
Geological Survey
Junior and Major Exploration and Mining Companies
Mining Companies
Mills and Metallurgists
Product Developers
Mills and Metallurgists

## Slide 15: Projects through the Exploration to Mining Value Chain
(100 – 500)
20
5
3
2
1
Progression of number of projects
5
10
20
50
100
Indicative cumulative cost per project (Varies from project to project) – INR Crores
15
Discovering and establishing a mineable deposit may cost between INR 1000 and 2000 crores
DISCOVERY

## Slide 16: Exploration Success is Rare
Over 200 kimberlitic rocks discovered in India; only one economic cluster
~ 2/3rd of the discoveries were in the previous MMDR regime by mining companies
~ 3/4th of diamond bearing kimberlites discovered by mining companies

## Slide 17: India’s Exploration Potential: India is Under-Explored
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015
Gold | 925.3 | 1071.7 | 849.7 | 508.8 | 509.2
PGM | 4.6 | 4.2 | 4.1 | 2.1 | 1.6
Copper | 489 | 571.7 | 355.8 | 284.5 | 201.6
Nickel | 203.2 | 224.3 | 166.6 | 138.6 | 125.9
Zinc-Lead | 115.3 | 136.4 | 97 | 57.2 | 50
U3O8 | 255.5 | 188.7 | 156 | 108.5 | 51.6
Diamonds | 7.1 | 12.9 | 9.5 | 6.5 | 7
Other | 261.7 | 304.3 | 253.5 | 148 | 121.5
Chart: GSI Budget ~ 20% for Survey and Early Exploration
| 2004-05 | 2005-06 | 2006-07 | 2007-08 | 2008-09 | 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 | 2014-15
GSI | 34.171 | 36.741 | 34.789 | 37.643 | 50.263 | 57.77 | 64.99 | 87.974 | 80.213 | 117.592 | 85.229
Global Exploration Expenditure (2011 – 2015)
India attracted < 0.5% of global exploration expenditure between 2000 - 2015

## Slide 18: Mineral Exploration Tools
Geological Mapping: Compass, microscope, toposheet
Geochemical Mapping: Sampler (manual or machine), analytical tools (XRD, XRF, AAS, ICP, MS, Proton Probe, Portable Probes), etc.
Geophysical Survey: Magnetometer, gravimeter, electrical survey tools, electromagnetic survey, reflection seismic survey, magneto- tellurics, down hole loggers, etc.
Remote Sensing: Multispectral data, hyperspectral data, LIDAR and other active sensor data, etc.
Drilling: Diamond core, Reverse Circulation, Rotary Air Blast, Sonic, Air Core, Coiled Tube, Auger, etc., etc.
The above tools are continuously improving in efficacy. Experienced mineral explorers use these tools appropriately to dynamically assess and manage investment risks, while progressing towards the discovery

## Slide 19: Exploration Specialists and Consultants
Based on:
Commodity
Mineralization style
Exploration tool applications
Terrain
Soil type / regolith
Geographies
Stage of exploration
CRIRSCO (JORC / SAMREC / NI 43-101 / NACRI) recognizes the specialisations and only allows Qualified Persons with demonstrated specific experience to sign off on specific exploration report for a specific stage
Exploration is a highly specialized activity. There are no “know all” exploration companies or exploration consultants available

## Slide 20: Prudent Mineral Exploration Policy for India

## Slide 21: India’s Mineral Security Needs in the 21st Century
Usage | Raw Materials
Infrastructure | Fe, Al, Mn, V, Cr, Ni, Cu, Pb, Zn, limestone, aggregates
Energy | Coal, hydrocarbons, U, Th
Energy supply | Cu, Al
Energy storage devices | REE, Nb, Ta, Graphite, Li, Ni, Co, Mn
Electric cars | REE, PGE, Sc, Al, Mg, Ti
Water desalination | PGE, Cr, Ti
Telecommunication infrastructure | Cu, Al, Ge
Cellphones | Ta, Nb, Sb
Transport systems | Al, Mg, Ti, Sc, Th, Re, Nb, Ni, Mo, Co, Sm
Paints | Ti, Cr
Moulds | Zr
Fertilizers | Potash, phosphate, boron
World is going through a revolutionary phase of development of new metallurgical process and metal product development phase for utilisation in future technologies
Most of the new age commodities occur as non-bulk mineralization in nature
India’s exploration for technology commodities would get a boost, if India starts investing in metallurgy and product development research
Elements in RED are no production; Elements in GREEN are short supply

## Slide 22: India’s Exploration Potential is Never in Doubt
India’s Obvious Geological Potential Map (GSI)
Continental Reconstructions : Gondwanaland and Rodinia
While GSI’s OGP is only 0.5 million km2, India’s real OGP is about 2 million km2 , Only about 15,000 sq kms area explored in detail

## Slide 23: MMDR 2015 and Impact of Auction Process Rigidity
GSI and Contractual Exploration Only and Refusal by Private Explorers to Participate
DISCOVERY
Feasibility
Development
Mining (Through Auctions)
VALUE
TIME
Current Auction Process Eliminates This Phase
Brownfield Exploration
Brownfield Mining
Concept (GSI / NMET)
Auctions have been designed to be transparent for investor and provide revenue maximization to the government
The Evidence of Mineral Content (EMC) Rule has been created to define auctionable blocks
EMC Rule eliminates Brownfield Opportunities in the asset

## Slide 24: Exploration in India – Post-MMDR 2015 (Amendment)
Exploration carried out by GSI and NMET funding. Some state DMGs have carried out additional exploration
Approximately 500 exploration programs since 2015. Over 2000 Crores spent (including wages and direct exploration expenditures on ground)
Bulk infrastructural commodities 50% of the programs by number and +75% by expenditure – coal, iron ore, bauxite, limestone, manganese
Non bulk tech commodity exploration programs include REE, base metals, precious metals, potash
Approximately 40 non-bulk exploration programs have moved to Geological Resource estimation stage. Approximately 100 exploration programs for bulk commodities have moved to resource estimation.
1 or 2 non-bulk deposits and about 20 bulk deposits may be declared economic by 2025.Mining if ever, would not start before 2030.
India needs significantly larger risky exploration investments from private sector and international explorers and miners to meet with India’s mineral development goals

## Slide 25: Mineral Exploration: What would attract Investors!
Sl | Requirements for a Competitive Exploration Investment Destination | Current Status in India
1 | Geological attractiveness | Y
2 | Explorability (terrain, soil cover, vegetation) | Y
3 | Freedom to select exploration target | N
4 | Security of Title – from exploration to mining | N
5 | Security of Tenure – at all stages | N
6 | Transparent and structured permitting process | Y / N
7 | Freedom to trade the exploration asset for profit | Y/N
8 | Availability of high quality digital survey data | Y
9 | Capital market support | N
10 | Fiscal incentives | N
To Create a Competitive Investment Regime
Non Negotiable

## Slide 26: Thank You
BROOKINGS INDIA
QUALITY. INDEPENDENCE. IMPACT